## Slide 1: High Frequency Amplifier
Group 9

## Slide 2: Brainstorming Sessions

## Slide 3: Circuit Diagram

## Slide 4: Calculations – Stage 1
Capacitor Selection
20 KHz = fmin RE = 66 ohm
XC2 < * RE
< * 66
C > 1.2 * 10-6 F
C = 1000 F
Resistor Selection
(Experimental value)
Ic = 20 mA (By observing datasheet)
VCE = 5V (Design Assumption)
Load line :
Ic = - * VCE + ( R= RE+RC)
RE+RC 360
Rc = 300 ohm RE = 66 ohm

## Slide 5
Biasing Resistors Selection
across RE
V=IR
VE -0 = 20mA * 66 ohm
VE = 1.32 V
Since VBE = 0.7 VB = 2.02 V
By Potential dividing rule
2.02 = (R8 / R8 + R7 ) * 12
R7 / R8 = 4.94059
R8 = 2 K ohm R7 = 8.8 K ohm

## Slide 6: AC Analysis
For first stage
rπ =
rπ = 309.4 ohm
(8.8k,2k, rπ are parallel to each other and 33 ohm is series to this parallel combination)
Zin = (8.8K//2K// rπ) + 33 ohm
Zin = 293.03 ohm
Open cct voltage gain
Avo (c)/ Zin
Avo 243.66

## Slide 7: Stage - 2

## Slide 8
RESULTS OBTAINED BY SIMUALTION
Parameter | Conditions | Min | Typ | Max | Unit
Operating Supply Voltage |  |  |  | 12 | V
Input Voltage (pk-pk) |  |  |  | 0.1 | V
Open Circuit Voltage Gain |  |  | 43.5 |  | 
Voltage Gain | RL = 8Ω |  | 42.5 |  | 
Power Gain |  |  | 33.3805 |  | dB
Bandwidth |  |  | 815.11 |  | kHz
Power Output | RL = 8Ω |  |  | 312 | mW
Load Current | RL = 8Ω |  |  | 197 | mA

## Slide 9: Waveforms Input – Channel A (blue) Output - Channel B (Red)

## Slide 10: Frequency Response

## Slide 11
Schematic and PCB Layout

## Slide 12
Schematic and PCB Layout
Schematic and PCB are designed with Altium 16.
Additionally, 12V DC fan is used
Two circuits have separate inputs and outputs.
70mm*75mm single layer PCB
PCB manufacturing method : Laser cutting (Engraving)

## Slide 14: ALTERNATIVE METHODS
Voltage Biasing
Resistor Biasing
Diode Biasing

## Slide 15
Voltage Biasing
Drawbacks
It is not practical to have extra batteries within the amplifiers output stage design

## Slide 16
Resistor Biasing
Drawbacks
Comparatively the gain is low.
Finding the exact resistor combination within the voltage divider network is troublesome.(solution: adjustable resistor set)
Since the biasing resistors’ resistance depend on the operating temperature, small change in the temperature may lead for a change in the quicent collector current.

## Slide 17
Diode Biasing
Drawbacks
Comparatively the gain is low.
Cannot be accurate about diode bias being 0.7V.

## Slide 18: Enclosure Design

## Slide 19: Work delegation
Name | Work done
K.N.S.Fernando | Circuit design, calculation
W.A.S.N.Jayawardena | Circuit simulations, calculation
R.G.H.V.Ratnayake | Enclosure design , simulation
G.K.H.Nadeeshan | Schematic & PCB, circuit design